- Historia do poste
        - Tecnologia de um poste
- Tecnologias de lampadas
- Consumos
- Custos associados
Lumen – (lm) measure of the total amount of visible light from a light source
Lumens per Watt (lm/W) useful way to measure the efficacy of lighting products
Gas-discharge lamps: family of artificial light sources that generate light by sending an electric discharge through an ionized gas

Through the system overview diagram, in figure \ref{fig:system_overview}, it is possible to identify the main modules of the system to be developed, and how they interact. We can divide the system into two subsystems: the local system, which represents a lamp post, and the remote system, that allows interaction with the system users.

\begin{figure}[ht]
\centering
\includegraphics[width=1\textwidth]{system_overview}
\caption{System Overview Diagram.}
\label{fig:system_overview}
\end{figure}

The local system is composed of sensors, a controller and a lamp. Regarding the sensors, there will be a motion detector, to allow the detection of movement in the vicinity of the pole, a light sensor, to detect the light conditions of the pole’s surroundings, a camera to find empty parking spots and a LED state sensor to know if the LED lamp is working. The controller, through sensors information, controls the luminosity of the lamp and communicates wirelessly with a remote server.
The remote server consists of a database that stores all information about each lamp post location and operating status. This information can be accessed through a mobile application by the operator responsible for the street lights network, in order to carry out the necessary maintenance of the lamp of each pole. In addition, the database stores information on free parking spaces. When a user wants to know where’s the closest free parking place, he can access a website that informs him of the number of free parking spaces in the nearest streets. Knowing that the public lighting network is directly related to the electrical network, this will be used to power local systems, such as the monitoring device. (Não vamos usar a rede eletrica no nosso prototipo)

\section{System Architecture}
Using the system overview diagram information, one can describe the system in two different architectures. Hardware architecture, as how the hardware modules interfaces with itself, and what are the physical components of the system, and software architecture, which details how the information is processed among different software layers.

\subsection{Hardware Architecture}
In figure \ref{fig:hw_arch}, one can see the diagram that represents the physical connections of the system. The Raspberry Pi is the main component in the system, processing all the information given by the sensors and controlling the \ac{led} lamp brightness. The power of most system components will be the output of the DC/DC converter, powering the Raspberry Pi and its associated sensors. In order to power the lamp and at the same time control its brightness, a driver must be used, taking the controller output and system power as inputs.