Network Architecture

The system to be developed is inserted in a network, more specifically, an infrastructure based network. This type of networks are composed by wireless segments of a more extensive network, whose core is usually a wired network. Infrastructure-based networks have a special station, called an Access Point (AP) or Base Station (BS), which serves as an interface between the wireless segment and the rest of the network. Inside the wireless segment, there will be a centralized communication, so that all messages that circulate on the network pass through a central station. That way, the network only supports two transmission directions: the downward direction (downlink), from the base station to the other stations, and the uplink direction, from the stations to the base station. The downlink usually allows the simultaneous transmission of information to a group of stations in the cell (multicast) or to all stations (broadcast).
Street lighting is generally divided into sectors, facilitating maintenance and problem solving regarding the lighting network. In figure [ref], one can see that the base station is a “special station”, since it connects the local network of lighting poles to other base stations, through a remote server, and also because it has a camera for the detection of available parking spaces. The rest of the stations that compose the local network, the local systems, will only do the smart management of their lamps.