In this section it will be specified the chosen hardware and the presented the interface between each of the components.

- Microp
The integrated circuit that will control the operating status of the remote will be the ATtiny85 [ref] (figure xx). This is a well known microcontroller due to its small dimensions, associated capabilities and its low price. Its a good fit for this system because of its low operating voltage and of its ability to read the data given by the sensors, the remote buttons, and produce an adequate response.

- Operating Supply Voltage: 1.8V to 5.5V
- 8 bit Microcontroller
- 8 pins, 6 GPIO pins;
- 8 kB of program memory size;
- 512 B data RAM size;

For programming the ATtiny85 it can be used an Arduino board, like Arduino UNO [ref], which is a one-time process.

- IR Emitter
The system’s actuator is an infrared emitter, which has been used in remote controls since the early 1980s. IR sensors are used to measure and detect infrared radiation in its surrounding environment. An IR emitter can be easily found, having the appearence represented in the figure [ref].

- Resistors
It is known that a light emitting diode (LED), like the IR emitter presented above, admits a maximum forward current. To do that, and as well as to control how much current flows through the remote button’s circuit, it may be used some resistors.

- Battery
In order to supply the system components, focusing on the microprocessor operating supply voltage, the system may be supplied by two or three batteries AAA, having in mind that each of this batteries works within the range 0.9 V to 1.5 V.

- SW Spec
To program the system’s microprocessor it can be used the Arduino Software (IDE) [ref], which is an open-source software, that makes it easy to write code and upload it to the board. This software can be used with any Arduino board, an so, adequate to program Arduino UNO.